## Slide 1: Tech Time
A discussion and Q&A about Tech for HRG

## Slide 2: What’s it all about, Alfa?
Tech is about getting you on track and home again, safely.
Reference materials
  GCR & Vintage GCR
    Both available at (SCCA.com – Programs – Road Racing – Rules)
    https://www.scca.com/pages/cars-and-rules.
    GCR sections 9.3 and 9.4
  Equipment Manufacturer’s Installation and Use instructions
  Common Sense

## Slide 3: Checklist
This handy checklist can help you make sure your car is ready for tech and track.
Expect it to be available:
  SCCA.com/roadracing and then click on Rules in the Road Race section.
  In the Technical Inspection Manual in your “file cabinet”
  Copy this screen NOW!

## Slide 4: Commonly Missed Items

## Slide 5: Cotter Pins and belt wrap
Courtesy of Schroth

## Slide 6: A Closer Look at Belts
FIA and SFI both certify belts
  Both are acceptable
  SCCA: Dec 31 of the year of Expiration
Expiration times can be different
  FIA: 5-years from date of manufacture
  SFI: It depends:
    5-years if no date of expiration
    2-years from date of manufacture if so stated
      SCCA end of the second calendar year
      SVRA and New Jersey: as stated on restraint
Some belt labels will have a “Not Valid After …” or “Valid Until …” date printed on them
As marked (5-YEARS)
2-YEARS
5-YEARS
As Marked

## Slide 7: Arm Restraints & Window Nets
Reduce the possibility of rolling over your arms.
Window Nets
  Must meet SFI 27.1 (SVRA enforces the 2-year expiration date)
  Must be mounted to drop down with release accessible to both driver and rescue worker
Arm restraints
  Required in open cars and others where a window net cannot be mounted
  Acceptable alternative to window nets for closed cars in SCCA vintage sanctioned races only
  Preferred in VRG
    Must meet SFI 3.3 for SVRA
    SCCA and VRG have no such SFI requirement
https://www.youtube.com/watch?v=OfWjXzvVoL0

## Slide 9: Batteries Not Tied Down and/or Insulated
Wet-cell batteries relocated to the PAX must be in a marine-type container.
  The only purpose of the container is to reduce acid splash onto the driver
The battery must be secured to the car independent of the container.
Lateral motion control as well as vertical hold down is a very very good idea, as are metal hold downs.

## Slide 10: Fire systems Not Maintained
It is required that your fire system be maintained per the manufacturers’ instructions
  Actuating heads lubed
  Actuating springs replaced
Safety pins on the bottle and actuating handle pulled before going on track!!!!
Handheld Fire Bottles should be replaced every 12 years per several manufacturers
Used New

## Slide 11: What times out?
SCCA enforces dates on
  Belts
  Helmets
Some other race organizations also enforce dates on
  HANS devices
  Window nets
Time takes its toll on fuel cells
  ATL recommends
    New foam every year
    New bladders after 5 years
James Ray

## Slide 12: Get that log book!
When buying a new-to-you vintage race car, be sure to get the original log book.
The date of issuance establishes the acceptable era of the roll cage and certain other safety equipment.
  Roll cage
  Fuel cell
If this is not available, then the cage and fuel cell must meet the current specifications in the GCR
An alternative is to use the log book from another VMC sanctioning body (VRG, SVRA, etc.) provided that the safety equipment reasonably conforms to date-of-issue SCCA specs. This will allow participation in Vintage Sanctioned SCCA events.

## Slide 13: Q & A
SCCA Tech Inspector